## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Chapter 4
© 2008 Pearson Education

## Slide 2
In Boolean algebra, a variable is a symbol used to represent an action, a condition, or data. A single variable can only have a value of 1 or 0.
Summary
Boolean Addition
The complement represents the inverse of a variable and is indicated with an overbar. Thus, the complement of A is A.
A literal is a variable or its complement.
Addition is equivalent to the OR operation. The sum term is 1 if one or more if the literals are 1. The sum term is zero only if each literal is 0.
Example
Determine the values of A, B, and C that make the sum term of the expression A + B + C = 0?
Solution
Each literal must = 0; therefore A = 1, B = 0 and C = 1.

## Slide 3
In Boolean algebra, multiplication is equivalent to the AND operation. The product of literals forms a product term. The product term will be 1 only if all of the literals are 1.
Summary
Boolean Multiplication
Example
What are the values of the A, B and C if the product term of A.B.C = 1?
Solution
Each literal must = 1; therefore A = 1, B = 0 and C = 0.

## Slide 4
Summary
Commutative Laws
In terms of the result, the order in which variables are ORed makes no difference.
The commutative laws are applied to addition and multiplication. For addition, the commutative law states
A + B = B + A
In terms of the result, the order in which variables are ANDed makes no difference.
For multiplication, the commutative law states
AB = BA

## Slide 5
Summary
Associative Laws
When ORing more than two variables, the result is the same regardless of the grouping of the variables.
The associative laws are also applied to addition and multiplication. For addition, the associative law states
A + (B +C) = (A + B) + C
For multiplication, the associative law states
When ANDing more than two variables, the result is the same regardless of the grouping of the variables.
A(BC) = (AB)C

## Slide 6
Summary
Distributive Law
The distributive law is the factoring law. A common variable can be factored from an expression just as in ordinary algebra. That is
AB + AC = A(B+ C)
The distributive law can be illustrated with equivalent circuits:
AB + AC
A(B+ C)

## Slide 7
Summary
Rules of Boolean Algebra
1. A + 0 = A
2. A + 1 = 1
3. A . 0 = 0
4. A . 1 = 1
5. A + A = A
7. A . A = A
6. A + A = 1
8. A . A = 0
9. A = A
=
10. A + AB = A(1+B) = A(1) = A
12. (A + B)(A + C) = A + BC
11. A + AB = A + B
6. A + A = 1
-

## Slide 9
Summary
Rules of Boolean Algebra
Rule 12, which states that (A + B)(A + C) = A + BC, can be proven by applying earlier rules as follows:
(A + B)(A + C) = AA + AC + AB + BC
= A + AC + AB + BC
= A(1 + C + B) + BC
= A . 1 + BC
= A + BC
This rule is a little more complicated, but it can also be shown with a Venn diagram, as given on the following slide…

## Slide 10
Summary
DeMorgan’s Theorem
The complement of a product of variables is equal to the sum of the complemented variables.
DeMorgan’s 1st Theorem
AB = A + B
Applying DeMorgan’s first theorem to gates:

## Slide 11
Summary
DeMorgan’s Theorem
DeMorgan’s 2nd Theorem
The complement of a sum of variables is equal to the product of the complemented variables.
A + B = A . B
Applying DeMorgan’s second theorem to gates:

## Slide 12
Summary
Apply DeMorgan’s theorem to remove the overbar covering both terms from the
expression X = C + D.
DeMorgan’s Theorem
Example
Solution
To apply DeMorgan’s theorem to the expression, you can break the overbar covering both terms and change the sign between the terms. This results in
X = C . D. Deleting the double bar gives X = C . D.
=

## Slide 13
Summary
Boolean Analysis of Logic Circuits
Combinational logic circuits can be analyzed by writing the expression for each gate and combining the expressions according to the rules for Boolean algebra.
Apply Boolean algebra to derive the expression for X.
Example
Solution
Write the expression for each gate:
Applying DeMorgan’s theorem and the distribution law:
C (A + B )
= C (A + B )+ D
(A + B )
X = C (A B) + D = A B C + D
X

## Slide 14
Summary
SOP and POS forms
Boolean expressions can be written in the sum-of-products form (SOP) or in the product-of-sums form (POS). These forms can simplify the implementation of combinational logic, particularly with PLDs. In both forms, an overbar cannot extend over more than one variable.
An expression is in SOP form when two or more product terms are summed as in the following examples:
An expression is in POS form when two or more sum terms are multiplied as in the following examples:
A B C + A B A B C + C D C D + E
(A + B)(A + C) (A + B + C)(B + D) (A + B)C

## Slide 15
Summary
SOP Standard form
In SOP standard form, every variable in the domain must appear in each term. This form is useful for constructing truth tables or for implementing logic in PLDs.
You can expand a nonstandard term to standard form by multiplying the term by a term consisting of the sum of the missing variable and its complement.
Example
Solution
Convert X = A B + A B C to standard form.
The first term does not include the variable C. Therefore, multiply it by the (C + C), which = 1:
X = A B (C + C) + A B C
= A B C + A B C + A B C

## Slide 16
Summary
POS Standard form
In POS standard form, every variable in the domain must appear in each sum term of the expression.
You can expand a nonstandard POS expression to standard form by adding the product of the missing variable and its complement and applying rule 12, which states that (A + B)(A + C) = A + BC.
Example
Solution
Convert X = (A + B)(A + B + C) to standard form.
The first sum term does not include the variable C. Therefore, add C C and expand the result by rule 12.
X = (A + B + C C)(A + B + C)
= (A +B + C )(A + B + C)(A + B + C)

## Slide 17
The Karnaugh map (K-map) is a tool for simplifying combinational logic with 3 or 4 variables. For 3 variables, 8 cells are required (23).
The map shown is for three variables labeled A, B, and C. Each cell represents one possible product term.
Each cell differs from an adjacent cell by only one variable.
Summary
Karnaugh maps

## Slide 18
Cells are usually labeled using 0’s and 1’s to represent the variable and its complement.
Gray code
Summary
Karnaugh maps
Ones are read as the true variable and zeros are read as the complemented variable.
The numbers are entered in gray code, to force adjacent cells to be different by only one variable.

## Slide 19
Summary
AB
AB
AB
AB
C C
Alternatively, cells can be labeled with the variable letters. This makes it simple to read, but it takes more time preparing the map.
Karnaugh maps
Read the terms for the yellow cells.
Example
Solution
The cells are ABC and ABC.

## Slide 20
1. Group the 1’s into two overlapping groups as indicated.
Read each group by eliminating any variable that changes across a boundary.
The vertical group is read AC.
Summary
K-maps can simplify combinational logic by grouping cells and eliminating variables that change.
Karnaugh maps
Group the 1’s on the map and read the minimum logic.
Example
B changes across this boundary
C changes across this boundary
Solution
The horizontal group is read AB.
X = AC +AB

## Slide 21
A 4-variable map has an adjacent cell on each of its four boundaries as shown.
Each cell is different only by one variable from an adjacent cell.
Grouping follows the rules given in the text.
The following slide shows an example of reading a four variable map using binary numbers for the variables…
Summary
Karnaugh maps

## Slide 22
X
Summary
Karnaugh maps
Group the 1’s on the map and read the minimum logic.
Example
1. Group the 1’s into two separate groups as indicated.
Read each group by eliminating any variable that changes across a boundary.
The upper (yellow) group is read as AD.
Solution
The lower (green) group is read as AD.
X = AD +AD
B changes
C changes
B changes
C changes across outer boundary

## Slide 23
Selected Key Terms
Variable
Complement
Sum term
Product term
A symbol used to represent a logical quantity that can have a value of 1 or 0, usually designated by an italic letter.
The inverse or opposite of a number. In Boolean algebra, the inverse function, expressed with a bar over the variable.
The Boolean sum of two or more literals equivalent to an OR operation.
The Boolean product of two or more literals equivalent to an AND operation.

## Slide 24
Selected Key Terms
Sum-of-products (SOP)
Product of sums (POS)
Karnaugh map
VHDL
A form of Boolean expression that is basically the ORing of ANDed terms.
A form of Boolean expression that is basically the ANDing of ORed terms.
An arrangement of cells representing combinations of literals in a Boolean expression and used for systematic simplification of the expression.
A standard hardware description language. IEEE Std. 1076-1993.

## Slide 25
1. The associative law for addition is normally written as
a. A + B = B + A
b. (A + B) + C = A + (B + C)
c. AB = BA
d. A + AB = A
© 2008 Pearson Education
Quiz

## Slide 26
2. The Boolean equation AB + AC = A(B+ C) illustrates
a. the distribution law
b. the commutative law
c. the associative law
d. DeMorgan’s theorem
© 2008 Pearson Education
Quiz

## Slide 27
3. The Boolean expression A . 1 is equal to
a. A
b. B
c. 0
d. 1
© 2008 Pearson Education
Quiz

## Slide 28
4. The Boolean expression A + 1 is equal to
a. A
b. B
c. 0
d. 1
© 2008 Pearson Education
Quiz

## Slide 29
5. The Boolean equation AB + AC = A(B+ C) illustrates
a. the distribution law
b. the commutative law
c. the associative law
d. DeMorgan’s theorem
© 2008 Pearson Education
Quiz

## Slide 30
6. A Boolean expression that is in standard SOP form is
a. the minimum logic expression
b. contains only one product term
c. has every variable in the domain in every term
d. none of the above
© 2008 Pearson Education
Quiz

## Slide 31
© 2008 Pearson Education
Quiz
7. Adjacent cells on a Karnaugh map differ from each other by
a. one variable
b. two variables
c. three variables
d. answer depends on the size of the map

## Slide 32
© 2008 Pearson Education
Quiz
8. The minimum expression that can be read from the Karnaugh map shown is
a. X = A
b. X = A
c. X = B
d. X = B

## Slide 33
© 2008 Pearson Education
Quiz
9. The minimum expression that can be read from the Karnaugh map shown is
a. X = A
b. X = A
c. X = B
d. X = B

## Slide 34
© 2008 Pearson Education
Quiz
10. In VHDL code, the two main parts are called the
a. I/O and the module
b. entity and the architecture
c. port and the module
d. port and the architecture

## Slide 35
Answers:
1. b
2. c
3. a
4. d
5. a
6. c
7. a
8. a
9. d
10. b
Quiz